## Slide 1
DATA TECHNICAL WORKSHOPTO IMPROVE THE REPORT OF FISHERY STATISTICS TO THE IOTC
Jakarta, Indonesia, 26 to 30 May 2025
Assing grids to your data with qgis

## Slide 2
OBJECTIVE
Provide a tutorial to obtain CWP grids for latitude and longitude positions to report Georeferenced catch and effort data (CE ) and Georeferenced size frequency data (SF) in line with IOTC data standard and spatial resolution required by CMM 15/02

## Slide 3
MATERIALS
Qgis software
Grid shapefiles from the IOTC data catalogue & Share point folder
IOTC Data Reference Catalogue v1.0 – Administrative and Geospatial Domains
Indian Ocean Regular Grids
5°x5° Grid
Un continents shapefile ( provided in Share point folder)
Simulated logbook data csv file (provided in Share point folder)

## Slide 4
QGIS is a free and open-source geographic information system (GIS) software, allowing users to analyze and edit spatial information, in addition to composing and exporting graphical maps.
Download Qgis at https://qgis.org/ and follow installation instructions

## Slide 5
Once installed, open the program and start a new project

## Slide 6
STEP 1 | LOAD DATA

## Slide 7
To load a new layer, you can do it from the main menu:
Layer/Data Source Manager
Or selecting the Data Source manager icon on the Toolbars menu

## Slide 8
The Data Source Manager menu pop-up giving options to incorporate on your map data from different formats
Select the option Vector to incorporate the base layers (land and grids) to your map.
Browse the menu Source (Vector dataset(s))to select your files location

## Slide 9
.shp (Shapefile): This is the main file containing the geometric information of the entities (points, lines, polygons).
.shx (Shape Index File): This is the index file that helps to access the geometric information of the .shp file more efficiently.
.dbf (dBASE File): This file contains the data table that stores the attributes associated to the geometric entities.
.prj (Projection File): This file specifies the reference coordinate system used for the layer.
A shapefile is a set of related files, typically including

## Slide 10
Select the file with .shp extension to add in your map

## Slide 11
Repeat the process for the land file (optional)

## Slide 12
Load the Simulated data csv file (Sets.csv), selecting delimited text format

## Slide 13
In the Geometry definition section, select LONG and LAT for X and Y fields , respectively.
Keep the rest of the parameters without changes

## Slide 14
Visualize your data points

## Slide 15
STEP 2 | PROCESS DATA

## Slide 16
To obtain the CWP grids you must realize a join between the attributes of the two files (Sets and Grids).
From the main menu select
Vector
Data Management tools
Join Attributes by Location

## Slide 18
To add the grid information to the Sets data select the Sets layer in the first drop-down menu “Join to features in”. To run this operation a spatial rule needs to be applied. Select intersect . Finaly choose the grids layer in “By comparing to” and click run.

## Slide 19
As result a new layer was added (Joined layer). You can verify that the grids codes were added to your records by right click/Open Attribute Table

## Slide 20
STEP 3 | VERIFY DATA

## Slide 21
To revise the Joined layer result you can follow to ways. First ensure that the layer is selected to be able to operate on it (click on it and you will see the blue color on the layer menu). Right click and select Zoom to layer from the menu to review the extend of your layer and identify outliers (out of range or land positions)

## Slide 22
The extend of the layer shows a point out of range (not in the Indian ocean)

## Slide 23
To clean the data, go to Open Attribute Table from the right click menu

## Slide 24
The pencil icon Toggle editing, allows edits on the table records. When activate the edition mode, select the record and then Delete selected features (bin icon). Save the changes

## Slide 25
Other option is active the edition mode selecting Toggle editing, from the right click menu

## Slide 26
Then select and delete the feature (point)

## Slide 27
Confirm and save the changes

## Slide 28
Using the tool identify Features of the main menu on top, allows the selection of a particular feature (point) for review

## Slide 29
When selecting, a window with all the information for this feature will be displayed on the right. With the aim to identify potential corrections a point with LAT = 0 (equator) was included for this exercise. In this case two grids were assigned for this location. For convention, you should choose the one that corresponds to North location (6100050) and remove the another one.

## Slide 30
STEP 4 | EXPORT DATA

## Slide 31
After clean the data, you can export it selecting Export/Save Feature As, from the right click menu.

## Slide 32
With the Save menu you can chose the format to export. You can select excel file to continue working on your data submission but note that the join layer is a temporal file. If you want to keep it save as a ESRI shapefile in your project and then export in the desire format

## Slide 33
The output file contains the original position and the associated grid.

## Slide 34
IOTC-Statistics@fao.org
Questions ?